Open Source Laptop Chassis expectations
known specs:
1. Design with FreeCAD
2. The PPC laptop motherboard will be designed to fit inside a classical 15,6 laptop chassis ( chassis must be selected before the end of 2018)
3. The LCD could be a B156HTN03.8 so a WUXGA 1920x1080 Full HD 15.6 inch
4. Probably the dvd will be not present
5. The motherboard have not the GPU but an MXM 3 interface to insert an MXM Video card ( probably the default AMD Embedded Radeon™ E9172 )
minimal:
1. Fit the PPC laptop motherboard ( sizes will arrive during Q1/2019)
2. Fit the MXM Video card ( depends from the video card selected)
3. Easily change the MXM Video Card
4. Easily change M.2 device
5. Easy change the DDR3L RAM
6. Easy change SSD/HDD
7. Same resistance of classical laptop chassis ( impact and thermal)
8. Possibility to print with a professional 3D printer ( with a lower possible cost)

welcome:
1. Stronger resistance than other laptop chassis
2. Fit the battery package (come from the classic notebook used for PPC laptop)
3. Fit the LCD (come from the classic notebook used for PPC laptop)
4. Fit the Keyboard and touchpad (come from the classic notebook used for PPC laptop)
5. Fit the heatsink (come from the classic notebook used for PPC laptop)
optimal:
1. Fit others motherboard
2. Parametric design able to scale to different lcd size
3. Fit others LCD changing the TOP or change only the frame for the LCD
4. Fit other battery package
5. Fit other keyboard and touchpad